## Slide 1
THURSDAY SESSION · WEEK 5
Basic Networking & Communication
IP addresses, subnets, and the tools that map a network
Tuesdays & Thursdays, 5:30-7:00 PM • Simons 281

## Slide 2
ATTENDANCE
Check in for tonight's meeting
Scan the QR code to sign in for attendance.
Requires your CofC login.
Can't scan? Go to forms.gle/ccN4CuqviXhndixq5
ATTENDANCE
CofC Cybersecurity Club
Scan to check in

## Slide 3
AGENDA
Tonight's agenda
From what an address means to what's plugged in
OSI vs. TCP/IP models
Seven layers on paper, four layers in practice.
What an IP address is
Dotted decimal, network and host portions.
Subnetting & private vs. public addresses
CIDR notation, masks, and RFC 1918 ranges.
Switches, routers, and ARP
Layer 2 vs. Layer 3, drawn out as an example.
Tool intro: ping, nc, curl, nmap, Wireshark, Packet Tracer
What each one is for.
Mapping the Range's network
Subnets and hosts pulled from the terraform.
Hardware option: physical lab network
Switches, cabling, and basic configuration.
Exercises on the Range
Scan, capture, build in Packet Tracer, and do the subnet math.
AGENDA
CofC Cybersecurity Club

## Slide 4
RECAP
Quick recap: reaching a host
Tuesday covered how SSH and RDP get you onto a host, once you already know its address. Carrying forward: what an address means and how traffic finds its way on a local network.
RECAP
CofC Cybersecurity Club

## Slide 5
THE OLDER MODEL
The OSI model
Seven layers
#
LAYER
KEY PROTOCOLS
7
Application
HTTP, HTTPS, DNS, SMTP, FTP
6
Presentation
JPEG, MPEG, TLS
5
Session
SOCKS, NetBIOS
4
Transport
TCP, UDP
3
Network
IP, ICMP, IGMP
2
Data Link
Ethernet, PPP, MAC
1
Physical
Cables, Signals
THE OSI MODEL
CofC Cybersecurity Club

## Slide 6
THE NEWER MODEL
The TCP/IP model
Four layers
LAYER
MAIN FUNCTIONS
EXAMPLES
Application
User services, data formatting
HTTP, HTTPS, DNS, SMTP, FTP
Transport
End-to-end delivery, reliability, ports
TCP, UDP
Internet
Logical addressing and routing
IP, ICMP, IGMP
Network Access
Framing, MAC addressing, signaling
Ethernet, Wi-Fi, ARP
THE TCP/IP MODEL
CofC Cybersecurity Club

## Slide 7
PUTTING THEM TOGETHER
OSI to TCP/IP mapping
The OSI model split some jobs TCP/IP considers as one layer
7
Application
6
Presentation
5
Session
4
Transport
3
Network
2
Data Link
1
Physical
Application
Transport
Internet
Network Access
OSI TO TCP-IP MAPPING
CofC Cybersecurity Club

## Slide 8
DEFINITION #1
What is an IP address?
An IPv4 address is a 32-bit number, written as four decimal numbers 0-255 separated by dots, that uniquely identifies a device on a network. Part of it names the network, part of it names the host.
32 bits, four octets
Each of the four numbers is 8 bits (0-255). The whole address is 32 bits total.
Network portion
Identifies which network a device belongs to, shared by every host on that subnet.
Host portion
Identifies one specific device within that network.
Subnet mask
Defines exactly where the network portion ends and the host portion begins.
WHAT IS AN IP ADDRESS
CofC Cybersecurity Club

## Slide 9
THE MATH
Subnetting basics
One example: 192.168.1.0/24
FIELD
VALUE
WHAT IT MEANS
CIDR notation
/24
The first 24 bits are the network portion, the remaining 8 are host bits.
Subnet mask
255.255.255.0
The same information as /24, written out as a full address.
Network address
192.168.1.0
All host bits set to 0. Identifies the network itself, not a usable host.
Broadcast address
192.168.1.255
All host bits set to 1. Reaches every host on the subnet at once.
Usable host range
192.168.1.1 - 192.168.1.254
Everything between network and broadcast, 254 usable addresses.
SUBNETTING BASICS
CofC Cybersecurity Club

## Slide 10
ADDRESSING CONVENTIONS
Private vs. public addresses
Some ranges are reserved and never routed on the open internet
RANGE
TYPE
NOTES
10.0.0.0/8
Private (RFC 1918)
10.0.0.0 - 10.255.255.255, the range the Range's whole VPC lives in.
172.16.0.0/12
Private (RFC 1918)
172.16.0.0 - 172.31.255.255, common in Docker and corporate networks.
192.168.0.0/16
Private (RFC 1918)
192.168.0.0 - 192.168.255.255, the default on most home routers.
127.0.0.0/8
Loopback
127.0.0.1 refers to "this machine," traffic never leaves the host.
169.254.0.0/16
Link-local (APIPA)
Self-assigned when a device can't reach a DHCP server.
PRIVATE VS PUBLIC
CofC Cybersecurity Club

## Slide 11
HOW LOCAL DELIVERY WORKS
Switches, routers, and ARP
Internetwork addresses (IP) vs intra network addresses (MAC)
Switch, Layer 2
Forwards frames within one network using MAC addresses, learned automatically as traffic passes through.
Router, Layer 3
Forwards packets between different networks using IP addresses, this is what a gateway does.
MAC address
A hardware address burned into the network interface. Unique per device, not tied to any one network.
ARP
Address Resolution Protocol, the question "who has this IP?" that maps an IP to a MAC on the local segment.
SWITCHES, ROUTERS, ARP
CofC Cybersecurity Club

## Slide 12
SEEING IT DRAWN OUT
An example network
Two PCs, a switch, and a router
Internet
Router
10.0.10.1
Switch
PC A
10.0.10.11
PC B
10.0.10.12
Both PCs are Layer 2 neighbors through the switch, same broadcast domain, no routing needed to reach each other. Reaching the internet means going through the router first, the default gateway.
EXAMPLE NETWORK DIAGRAM
CofC Cybersecurity Club

## Slide 13
TOOL INTRO
ping: the simplest reachability check
Sends an ICMP echo request, waits for an echo reply, times the round trip
ping 10.0.10.5 64 bytes from 10.0.10.5: icmp_seq=1 ttl=64 time=0.412 ms 64 bytes from 10.0.10.5: icmp_seq=2 ttl=64 time=0.389 ms 64 bytes from 10.0.10.5: icmp_seq=3 ttl=64 time=0.401 ms
•
No reply at all usually means a firewall is dropping ICMP, not necessarily that the host is down.
•
TTL tells you roughly how many hops away the host is, it decrements by one at every router.
TOOL INTRO: PING
CofC Cybersecurity Club

## Slide 14
TOOL INTRO
nc: netcat, the network Swiss Army knife
Opens raw TCP or UDP connections, reads and writes to them directly
Banner grab
nc -v 10.0.10.10 80
Connect to a port and see what the service says first, no browser needed.
Quick listener
nc -lvp 4444
Listen on a port, useful for testing whether traffic is arriving.
Port check
nc -zv 10.0.10.5 22
Zero-I/O mode, just report whether the port is open, nothing sent.
TOOL INTRO: NC
CofC Cybersecurity Club

## Slide 15
TOOL INTRO
curl: talking HTTP directly
Makes web requests from the command line without a browser
Fetch a page
curl http://10.0.10.10
Prints the response body straight to the terminal, the same thing a browser would render.
Just the headers
curl -I http://10.0.10.10
HEAD request, headers only, a fast way to check a web server's software banner.
Verbose mode
curl -v https://10.0.10.10
Shows the TCP connect, TLS handshake, request, and response, all in one place.
TOOL INTRO: CURL
CofC Cybersecurity Club

## Slide 16
TOOL INTRO
nmap: finding what's on a network
Network Mapper. Scans a range of addresses for live hosts, open ports, and services.
nmap -sn 10.0.10.0/24 # ping sweep, just find live hosts nmap -p 22,80,443 10.0.10.5 # scan specific ports on one host nmap -sV 10.0.10.5 # guess service versions on open ports
Start broad (a sweep across the whole subnet), then narrow in on one host.
TOOL INTRO: NMAP
CofC Cybersecurity Club

## Slide 17
TOOL INTRO
Wireshark: capturing network traffic
Captures and decodes packets live
Capture filters
Applied before capture starts, limits what gets recorded. Example: port 22
Display filters
Applied after the fact, hides rows without discarding data. Example: tcp.port==22
Follow TCP Stream
Reassembles one conversation's packets into the data that was sent.
Common display filters:
ip.addr==10.0.10.5
Only traffic to or from this host
tcp.port==22
Only SSH traffic
http
Only HTTP requests and responses
icmp
Only ping traffic
TOOL INTRO: WIRESHARK
CofC Cybersecurity Club

## Slide 18
TOOL INTRO
Packet Tracer: designing a network before you build it
A free simulator from Cisco's Networking Academy
Drag-and-drop switches, routers, and PCs, wire them together, then test connectivity, without touching hardware. Useful for planning the physical lab layout before wiring anything. Commonly used in industry to plan before execution.
Free to use
Available through a Cisco Networking Academy / Skills for All account, no cost.
Simulation mode
Watch packets move hop by hop, useful for seeing how traffic will flow on your network.
Good for planning
Good for catching issues before spending money on hardware.
TOOL INTRO: PACKET TRACER
CofC Cybersecurity Club

## Slide 19
APPLYING IT
Mapping the Range's network
What a ping sweep of the blue subnet finds
IP ADDRESS
HOST
OS / DISTRO
10.0.10.5
Blue DNS
Debian
10.0.10.10
Blue Webserver
Ubuntu
10.0.10.20
Blue CentOS DB
CentOS
10.0.10.30
Blue CentOS Samba
CentOS
10.0.10.40
Blue Ubuntu Mail
Ubuntu
10.0.10.50
Blue Windows DB
Windows Server
10.0.10.60
Blue Windows AD
Windows Server
10.0.10.80
Blue Ubuntu
Ubuntu
All inside 10.0.10.0/24, the blue subnet, one of three carved out of the Range's 10.0.0.0/16 VPC.
MAPPING THE RANGE
CofC Cybersecurity Club

## Slide 20
HARDWARE
Connecting the club's lab network, Part 1
Switches and cabling, before anything gets configured
1
Start with a diagram
Sketch it before implementing.
2
Connect switches to switches
3
Connect PCs to access ports
Each lab machine gets its own port using a straight-through Ethernet cable.
4
Confirm link lights
A solid or blinking light on both ends means Layer 1 is good.
A simple topology to start from
One core switch, uplinked to two or three access switches, each access switch feeding a handful of lab PCs. No routing needed yet, just Layer 2 end to end.
PHYSICAL LAB NETWORK, PART 1
CofC Cybersecurity Club

## Slide 21
HARDWARE
Connecting the club's lab network, Part 2
Assigning addresses and proving the physical path
5
Assign static IPs
Pick a private range for the lab, e.g. 192.168.50.0/24, and give each machine an address by hand.
6
Verify with ping
ping between two machines confirms Layer 3 works end to end.
7
Trace the physical path
Follow each cable by hand, PC to switch port to uplink. Label anything that isn't labeled yet.
sudo ip addr add 192.168.50.10/24 dev eth0 sudo ip link set eth0 up ping 192.168.50.11 traceroute 192.168.50.11
traceroute won't show intermediate hops on a flat Layer 2 network. This is expected and confirms there's no router in between.
PHYSICAL LAB NETWORK, PART 2
CofC Cybersecurity Club

## Slide 22
TONIGHT'S PRACTICE
Tonight's exercises
Four demos
1
Scan the blue subnet
Run an nmap ping sweep against 10.0.10.0/24 and list every live host you find.
2
Capture and identify
Start a Wireshark capture, generate some traffic, and find it in the capture.
3
Subnet math, by hand
Given an IP and a CIDR, work out the network, broadcast, and usable range.
4
Build it in Packet Tracer
Recreate tonight's physical lab layout as a topology, bonus: make it route.
TONIGHT'S EXERCISES
CofC Cybersecurity Club

## Slide 23
EXERCISE 1
Scan the blue subnet
Find every live host
1
Connect to the Range
2
Run a ping sweep
nmap -sn 10.0.10.0/24
3
Record what you find
Hostname and IP for every host that responds.
4
Scan one host's ports
nmap -p- 10.0.10.5
Nmap scan report for 10.0.10.5 Host is up (0.0012s latency). Nmap scan report for 10.0.10.10 Host is up (0.0009s latency).
EXERCISE 1
CofC Cybersecurity Club

## Slide 24
EXERCISE 2
Capture and identify a protocol
Watch your own traffic leave the machine and come back
1
Start a capture
Pick your active interface in Wireshark and start capturing.
2
Generate traffic
ssh into a Range host, or just ping one, from another terminal.
3
Stop and filter
Apply tcp.port==22 or icmp to isolate what you just generated.
4
Find the handshake
Locate the SYN, SYN-ACK, ACK sequence that opens the TCP connection.
WHAT SUCCESS LOOKS LIKE
Three packets in a row: your machine's SYN, the target's SYN-ACK, and your machine's final ACK, all before any actual SSH data moves. The same handshake TCP uses everywhere, not just SSH.
EXERCISE 2
CofC Cybersecurity Club

## Slide 25
EXERCISE 3
Subnet math
GIVEN
172.16.40.0/22
Subnet mask
Network address
Broadcast address
Usable host range
Total usable hosts
Work it out on paper, then compare answers as a group.
EXERCISE 3
CofC Cybersecurity Club

## Slide 26
EXERCISE 4
Build it in Packet Tracer
1
Place the devices
Drag two PCs, one switch, and one router onto the canvas.
2
Cable it up
Copper straight-through from each PC to the switch, switch to the router's LAN port.
3
Assign IP addresses
Same subnet for both PCs and the router's LAN interface, e.g. 10.0.10.0/24.
4
Test in Realtime mode
Open a PC's Command Prompt and ping the other PC, then ping the router.
5
Switch to Simulation mode
Re-run the ping and watch the packet hop from PC to switch to PC.
BONUS
Add a second switch and a second pair of PCs on a different subnet, then configure the router to route between them. If PCs on both sides can ping each other, it works.
EXERCISE 4
CofC Cybersecurity Club

## Slide 27
WHERE THIS CAME FROM
Resources & citations
ISO/IEC 7498-1: The OSI reference model
iso.org/standard/20269.html
RFC 1122: Requirements for Internet Hosts
rfc-editor.org/rfc/rfc1122
RFC 791: Internet Protocol
rfc-editor.org/rfc/rfc791
RFC 1918: Private address space
rfc-editor.org/rfc/rfc1918
RFC 792: Internet Control Message Protocol
rfc-editor.org/rfc/rfc792
nmap: reference guide
nmap.org/book/man.html
Netcat (nc): man page
man.openbsd.org/nc
curl: everything curl
everything.curl.dev
Wireshark: user's guide
wireshark.org/docs/wsug_html_chunked
Cisco Packet Tracer, Skills for All
skillsforall.com
MITRE ATT&CK: Network Service Discovery
attack.mitre.org/techniques/T1046
RESOURCES
CofC Cybersecurity Club

## Slide 28
NEXT SESSION
Tuesday: Operating System Permissions & Access Control
You now know how a packet finds its way to a host. Next up: what happens once it gets there, user accounts, groups, and who's allowed to do what.
Simons 281, College of Charleston
Tuesdays & Thursdays, 5:30-7:00 PM
Questions on tonight's exercises? Ask in #defense-team
NEXT UP
CofC Cybersecurity Club