## Slide 1
TUESDAY SESSION · WEEK 11
Network Monitoring
Packet structures, protocol headers, and what normal traffic looks like
Tuesdays & Thursdays, 5:30-7:00 PM • Simons 281

## Slide 2
ATTENDANCE
Check in for tonight's meeting
Scan the QR code to sign in for attendance.
Requires your CofC login.
Can't scan? Go to forms.gle/ccN4CuqviXhndixq5
ATTENDANCE
CofC Cybersecurity Club
Scan to check in

## Slide 3
AGENDA
Tonight's agenda
Ethernet frames
IPv4 Headers
TCP and UDP headers
Two most important packet types.
Encapsulation
How a frame, a packet, and a segment nest inside each other.
tcpdump
Capturing traffic from the command line.
tcpdump vs. Wireshark
Two tools to inspect network traffic.
Common ports
Widely used ports and what they’re used for.
What normal traffic looks like
Hardware option: a monitoring link
Mirroring traffic off the lab switch.
AGENDA
CofC Cybersecurity Club

## Slide 4
RECAP
Quick recap: hunting on the host
The last two meetings covered what runs on a host, and how to find what should not be there. Tonight we will discuss networks and inspecting network traffic.
RECAP
CofC Cybersecurity Club

## Slide 5
DEFINITION #1
What is network monitoring?
Every packet is visible, whether the application that sent it wanted you to see it or not. It is easy to capture traffic, but often much harder to inspect its contents (encryption).
Passive
Capturing a copy of traffic. Nothing about the conversation changes because you are watching.
Every layer at once
A single capture shows the Ethernet frame, the IP packet, and the segment inside it. You have to filter further for what you want.
WHAT IS NETWORK MONITORING
CofC Cybersecurity Club

## Slide 6
PACKET STRUCTURES
Ethernet frames
Layer 2 over RJ45. Everything else found inside the payload.
Dest MAC
6 bytes
Src MAC
6 bytes
EtherType
2 bytes
Payload
46-1500 bytes
FCS
4 bytes
Dest / Src MAC
The physical hardware addresses of the next hop, not the final destination. These change at every router.
EtherType
Names the protocol contained inside. 0x0800 means IPv4 is next.
FCS
A checksum covering the whole frame. A NIC drops anything that fails it before it reaches software.
Source: IEEE 802.3, Ethernet standard. RFC 894. CSCI 345 Networking Reference, Network Packet Structure.
THE ETHERNET FRAME
CofC Cybersecurity Club

## Slide 7
PACKET STRUCTURES
IPv4 headers
Twenty bytes, five rows of 32 bits each
Ver
4b
IHL
4b
Type of Service
8b
Total Length
16b
Identification
16b
Flg
3b
Fragment Offset
13b
TTL
8b
Protocol
8b
Header Checksum
16b
Source IP Address
32 bits
Destination IP Address
32 bits
TTL
Decrements at every router. Packet dies when this reaches 0. Stops routing loops from lasting forever.
Protocol
Names what is inside: 6 for TCP, 17 for UDP, 1 for ICMP.
Fragment fields
Handle a packet too large for one link, split at the IP layer and reassembled at the destination.
Source: RFC 791, Internet Protocol. CSCI 345 Networking Reference, IPv4 Packet Structure.
THE IPV4 HEADER
CofC Cybersecurity Club

## Slide 8
PACKET STRUCTURES
TCP headers
Twenty bytes minimum. Many mechanisms to ensure delivery.
Source Port
16b
Destination Port
16b
Sequence Number
32 bits
Acknowledgment Number
32 bits
Off
4b
Res
3b
Flags
9b
Window Size
16b
Checksum
16b
Urgent Pointer
16b
Flags: NS CWR ECE URG ACK PSH RST SYN FIN, nine single bit switches. SYN and ACK together open a connection. FIN closes one.
Sequence and acknowledgment numbers are what let TCP detect a dropped segment and ask for it again. UDP has neither. Commonly used where packet loss is unacceptable (e.g., messaging, file transfer, email).
Source: RFC 9293, Transmission Control Protocol (TCP). CSCI 345 Networking Reference, TCP Packet Structure.
THE TCP HEADER
CofC Cybersecurity Club

## Slide 9
PACKET STRUCTURES
UDP headers
Eight bytes fixed.
Source Port
16 bits
Destination Port
16 bits
Length
16 bits
Checksum
16 bits
That is the entire header. No sequence numbers, no acknowledgment, no window size. UDP hands a packet to the network and moves on, which is exactly why it is faster and why DNS, DHCP, and NTP all use it. Commonly used where packet loss is acceptable and latency is more important (e.g., gaming, video calls).
Source: RFC 768, User Datagram Protocol. CSCI 345 Networking Reference, UDP Packet Structure.
THE UDP HEADER
CofC Cybersecurity Club

## Slide 10
PACKET STRUCTURES
Encapsulation: how it all nests
Each layer wraps the one above it, and gets a new name for doing it
Data
Application
The raw bytes an app wants to send. An HTTP request, for example.
→
Segment
Transport, TCP
TCP wraps it with a header: ports, sequence number, flags.
→
Packet
Internet, IP
IP wraps that with source and destination addresses.
→
Frame
Network Access
Ethernet wraps that with MAC addresses and a checksum.
Each name describes what exists at that point, not a different piece of data. A frame contains a packet contains a segment contains your data, one inside the next.
Frame [ Ethernet header [ IP header [ TCP header [ Data ] ] ] FCS ]
Source: CSCI 345 Networking Reference, PDU Terminology (What We Call It When).
ENCAPSULATION
CofC Cybersecurity Club

## Slide 11
TOOLS
tcpdump: capturing traffic from the command line
No GUI required.
tcpdump -i eth0 # capture everything on this interface tcpdump -i eth0 -n port 443 # only traffic on port 443, skip DNS lookups on the output tcpdump -i eth0 -w capture.pcap # write to a file instead of printing tcpdump -r capture.pcap -X # read it back, hex and ASCII side by side
Source: tcpdump(1), man page, tcpdump.org.
LINUX
TCPDUMP
CofC Cybersecurity Club

## Slide 12
TOOLS
tcpdump vs. Wireshark
Same captures, different jobs
TCPDUMP
WIRESHARK
Interface
Command line, text output
Graphical, point and click
Best for
A remote server over SSH, or scripting a capture
Deep inspection of one conversation
Filter syntax
Berkeley Packet Filter, e.g. tcp port 443
Display filters, e.g. tcp.port == 443
Typical workflow
Capture with tcpdump, then open the file in Wireshark
Capture and inspect in the same window
TCPDUMP VS WIRESHARK
CofC Cybersecurity Club

## Slide 13
SETTING A BASELINE
Common ports
20, 21
TCP
FTP
File Transfer
22
TCP
SSH, SFTP
Secure Shell
25
TCP
SMTP
Email
53
UDP/TCP
DNS
Domain Name
67, 68
UDP
DHCP
IP Configuration
80
TCP
HTTP
Web
110
TCP
POP3
Email
123
UDP
NTP
Time Sync
143
TCP
IMAP
Email
443
TCP
HTTPS
Secure Web
3306
TCP
MySQL
Database
5432
TCP
PostgreSQL
Database
Source: CSCI 345 Networking Reference, Common Ports. IANA Service Name and Transport Protocol Port Number Registry.
COMMON PORTS
CofC Cybersecurity Club

## Slide 14
SETTING A BASELINE
What normal traffic looks like
ARP
"Who has this IP?" broadcasts. Constant on any local segment, and completely normal.
DNS, UDP 53
A steady trickle of lookups. Every hostname a device touches starts here.
TCP three way handshake
SYN, SYN-ACK, ACK, over and over, on port 443 more than anywhere else.
DHCP, UDP 67/68
Bursts when a device joins the network or renews its lease.
mDNS / SSDP
Devices announcing themselves for local discovery. Common on any LAN with more than a few devices.
Source: IANA Service Name and Transport Protocol Port Number Registry. RFC 826, An Ethernet Address Resolution Protocol.
WHAT NORMAL TRAFFIC LOOKS LIKE
CofC Cybersecurity Club

## Slide 15
HARDWARE OPTION
Connecting a monitoring link, Part 1
Getting a copy of traffic without sitting in its path
1
Pick a SPAN capable switch
Not every switch can mirror traffic. Check for a SPAN or port mirroring feature first.
2
Choose the source port
The uplink or the port carrying the traffic you want to see.
3
Choose the destination port
Where your laptop plugs in. It only receives, it does not participate in the network.
4
Configure the mirror
Switch specific, but the idea is the same everywhere: copy source port traffic to destination port.
MONITORING LINK, PART 1
CofC Cybersecurity Club

## Slide 16
HARDWARE OPTION
Connecting a monitoring link, Part 2
SPAN port vs. a dedicated tap
SPAN PORT
NETWORK TAP
What it is
A feature built into a switch, copies traffic to another port
A separate physical device the link runs through
Cost
Free, if the switch supports it
An extra piece of hardware to buy
Under load
Can drop packets if the switch is busy
Sees everything, a tap does not prioritize its own management traffic
Setup
A configuration change on the switch
Physically inline, briefly interrupts the link to install
MONITORING LINK, PART 2
CofC Cybersecurity Club

## Slide 17
TONIGHT'S PRACTICE
Tonight's exercises
Three passes: capture, read, and baseline
1
Capture and identify a handshake
Run tcpdump on a Range host, generate an SSH connection, find the SYN, SYN-ACK, ACK.
2
Decode a header from a live capture
Open one packet in Wireshark and confirm every field against the diagram.
3
Baseline a Range subnet
Capture five minutes of traffic on the blue subnet, write down what is normal.
TONIGHT'S EXERCISES
CofC Cybersecurity Club

## Slide 18
EXERCISE 1
Capture and identify a handshake
Watch a connection open:
1
Start a capture
sudo tcpdump -i eth0 -n tcp port 22
2
Generate traffic
From another terminal, ssh into the same host
3
Find the SYN
Flags [S], the client's opening move
4
Find the SYN-ACK
Flags [S.], the server answering
5
Find the final ACK
Flags [.], the handshake completing
Three packets, in order, before any actual SSH data moves. Used to establish a TCP connection.
LINUX
EXERCISE 1
CofC Cybersecurity Club

## Slide 19
EXERCISE 2
Decode a header from a live capture
Wireshark breaks the bytes out for you, confirm it against the diagram from earlier
1
Start a capture
Wireshark, pick your active interface
2
Filter it down
tcp.port == 443 in the display filter bar
3
Open one packet
Click it, expand "Internet Protocol Version 4" in the packet details pane
•
Confirm Version reads 4, and Header Length reads 20 bytes, no options.
•
Check Time to Live. How many hops away does that suggest the source is.
•
Confirm Protocol reads TCP (6), matching what shows up further down the tree.
•
Read Source and Destination Address directly. Wireshark has already done the byte counting.
EXERCISE 2
CofC Cybersecurity Club

## Slide 20
EXERCISE 3
Inspect a Range subnet
1
Capture
tcpdump -i eth0 -n -w baseline.pcap for five minutes
2
Open in Wireshark
Statistics > Protocol Hierarchy for the big picture
3
List findings
Protocols, ports, hosts
EXERCISE 3
CofC Cybersecurity Club

## Slide 21
WHERE THIS CAME FROM
Resources & citations
CSCI 345 Networking Reference
Course material, packet structures & ports
RFC 791: Internet Protocol
rfc-editor.org/rfc/rfc791
RFC 9293: Transmission Control Protocol
rfc-editor.org/rfc/rfc9293
RFC 768: User Datagram Protocol
rfc-editor.org/rfc/rfc768
RFC 894: IP Datagrams over Ethernet
rfc-editor.org/rfc/rfc894
RFC 826: Address Resolution Protocol
rfc-editor.org/rfc/rfc826
IEEE 802.3, Ethernet standard
ieee802.org/3
tcpdump(1), man page
tcpdump.org
IANA Port Number Registry
iana.org/assignments/service-names-port-numbers
RESOURCES
CofC Cybersecurity Club

## Slide 22
NEXT SESSION
Thursday: Analyzing Traffic for Incidents
You now know how to read a packet and what normal looks like. Thursday is about finding what does not fit: unencrypted credentials, and scanning signatures.
Simons 281, College of Charleston
Tuesdays & Thursdays, 5:30-7:00 PM
Questions on tonight's exercises? Ask in #defense-team
NEXT UP
CofC Cybersecurity Club